## Slide 1
Portal
Portal
Transmitter
Declaration
Transmitter
IEEE 802.11
Distribution System
Access
Point
uplink
downlink
Receiver
Consider a Transmission Scenario with a group of Receivers
Video files are transmitted from the transmitter side, through the AP, and to the receivers.
The declaration and handshake processes are not considered
Application Scenario

## Slide 2
Overview of Evalvid

## Slide 3
Encodes function
  H.263 (ffmpeg, DResearch)
  MPEG-4 (ffmpeg, XviD)
  H.264 (x264, JM 10.2)
The size of codecs file under 264 is 16413KB
Bit-rate 128kbps
Frames per second 30FPS
An I-frame every second 30GOP
Max. packet size 1472 MTU

## Slide 4
Channel: wireless channel
Propagation model: tworay ground
Physics layer type: wireless pyh extension
Mac layer: 802_11extension
Queueing method at the interface: priority queue which gives priority to the routing protocol packets
Antenna: Omni-directional Antenna
Routing protocol: DumbAgent (it means the source and receiver are neighbours which can be touched within one hop)
802_11 datarate: 54Mb
Application layer traffic setting: packet size 1023 bytes, rate 256Kb

## Slide 5
802.11a setting
CSThresh_ 6.31e-12 ;#-82 dBm Wireless interface sensitivity (sensitivity defined in the standard)
Pt_ 0.001
freq_ 5.18e+9
set noise_floor_ 2.512e-13 ;#-96 dBm for 10MHz bandwidth
L_ 1.0 ;#default radio circuit gain/loss
PowerMonitorThresh_ 1.259e-13 ;#-99dBm power monitor sensitivity
HeaderDuration_ 0.000020 ;#20 us
BasicModulationScheme_ 0
PreambleCaptureSwitch_ 1
set DataCaptureSwitch_ 0
SINR_PreambleCapture_ 2.5118; ;# 4 dB
SINR_DataCapture_ 100.0; ;# 10 dB
set trace_dist_ 1e6 ;# PHY trace until distance of 1 Mio. km ("infinty")
PHY_DBG_ 0
set CWMin_ 15
CWMax_ 1023
SlotTime_ 0.000009
set SIFS_ 0.000016
set ShortRetryLimit_ 7
set LongRetryLimit_ 4
set HeaderDuration_ 0.000020
set SymbolDuration_ 0.000004
set BasicModulationScheme_ 0
set use_802_11a_flag_ true
set RTSThreshold_ 2346
set MAC_DBG 0